## Slide 1: Diode Exercise 2

## Slide 2: Homework

## Slide 3: Find V and I with Ideal and Practical Model

## Slide 4: V-I Characteristic: V = f(I)
Q point: A point with specific current and voltage of the diode in a specific circuit analysis

## Slide 5: Example for Real V-I Diode
Determine VD,ID and VR:
  Vd + I*R = E -> Vd = E – I*R -> y = 10 – x*0.5kOhm

## Slide 6: Answer
At Q-point: VD= 0.78V

## Slide 7: Zener Diode
Forward Bias: Normal diode
Reverse Bias: The voltage is kept at a constant value

## Slide 8: Exercise
Find I and IL

## Slide 9: Answer
I = (120-50)/R = 14mA
IL = 50/RL = 50/10k = 5mA
IZ = 14 – 5 = 9mA

## Slide 10: Exercise
The load current is to vary from 12 to 100 mA.
The input voltage is constant at 12V and the minimum zener current is 10 mA.
Find the value of series resistance R to maintain a voltage of 7.2 V across the load.

## Slide 11: Answer
VR = 12 – 7.2 = 4.8V
The minimum zener current will occur when the load current is maximum:
R < = 4.8 / (10 + 100)mA = 43.5 OhM

## Slide 12: Exercise
The minimum Zener current is 200 mA.
The input voltage is vary from 22V to 28V

## Slide 13: Answer
The zener current will be minimum (i.e. 200 mA) when the input voltage is minimum (i.e. 22 V)
IL = 1000mA
R = (22 – 18)/ (200 + 1000) = 3.33 Ohm

## Slide 14: Exercise
The input voltage varies between 13 V and 16 V
The load current varies between 10 mA and 85 mA
The minimum zener current is 15 mA
Calculate the value of series resistance R

## Slide 15: Answer
R = 30 Ohm

## Slide 16: Exercise
Zener is 15V
IZ = 200mA
IL = 100mA
Calculate R?