## Slide 1: JFET Exercise

## Slide 2: Remind…
Saturation
Pinch-off voltage
Cut off
Breakdown

## Slide 3: For a JFET, the value of VDS at which ID becomes essentially constant is the
pinch-off voltage.
cutoff voltage.
breakdown voltage.
ohmic voltage.

## Slide 4: A JFET data sheet specifies VGS(off) = –10 V and IDSS = 8 mA. Find the value of ID when VGS = –3 V.
2mA
1.4mA
4.8mA
3.92mA

## Slide 5: Find ID
A JFET data sheet specifies VGS(off) = –6 V and IDSS = 8 mA. Find the value of ID when VGS = –3 V.
2mA
4mA
8mA
None of these above

## Slide 6: On the drain characteristic curve of a JFET for VGS = 0, the pinch-off voltage is
below the ohmic area.
between the ohmic area and the constant current area.
between the constant current area and the breakdown region.
above the breakdown region.

## Slide 7: The value of VGS that makes ID approximately zero is the
pinch-off voltage.
cutoff voltage.
breakdown voltage.
ohmic voltage.

## Slide 8: What is the value of IG
0mA
2mA
4mA
6mA
Notes: 0mA

## Slide 9: Determine VDS
0V
2V
4V
-2V

## Slide 10: Determine the value of VS.
20V
8V
6V
2V

## Slide 11: A self-biased n-channel JFET has a VD = 6 V. VGS = –3 V. Find the value of VDS.
In a self bias configuration VG = 0V and there is a Resistor RS, connected to the Ground

## Slide 12: ID = 6 mA. Calculate the value of VDS
-9V
9V
6V
3V

## Slide 13: Refer to the given figure. ID = 6 mA. Calculate the value of VDS.
-6V
6V
12V
-3V

## Slide 14: Refer to figure given below. Determine the value of VGS.
-20V
-8V
-6V
-2V

## Slide 15: What type(s) of gate-to-source voltage(s) can a depletion MOSFET (D-MOSFET) operate with?
Zero
Positive
Negative
Any of the above