## Slide 1: CO2015 Introduction to Transistors and Applications

## Slide 2: What is Transistor?
Transistor is a semiconductor device used to:
  Amplifier signal
  Switch signal or electrical power
There are two types of basic transistor out there: Bi-Polar Junction (BJT) and Metal-Oxide Field-Effect (MOSFET)

## Slide 3: Bipolar Junction Transistor
Bi-polar Junction Transistor (BJT)
Collector (C), Base (B), and Emitter (E)

## Slide 4: Transistor = 2 Diodes
Checking transistors is similar to diodes
Pin order: ECB or BCE

## Slide 5: Exercise
From these measurements, determine what type of BJT this is (PNP or NPN)

## Slide 6: Answer
PNP transistor

## Slide 7: Saturation Mode
Saturation is the ON MODE of a transistor
A transistor in saturation mode acts like a short circuit between collector and emitter

## Slide 8: Cut-Off Mode
Cutoff mode is the opposite of saturation
There is no collector current, and therefore no emitter current
It almost looks like an open circuit

## Slide 9: Applications I: Switches
When the voltage at the base is greater than 0.6V, the transistor starts saturating  short circuit
When the voltage at the base is less than 0.6V the transistor is in cutoff mode  open circuit
Low-side switch

## Slide 10: Applications I: Switches
High side switch
PNP transistor: Control signals are reversed
A transistor without a resistor on the base is like an LED with no current-limiting resistor

## Slide 11: Logic Gate - NOT

## Slide 12: Logic Gates

## Slide 13: Logic Gate

## Slide 14: H-Bridge

## Slide 15: Oscillator
Q2 ON – Q1 OFF
VBE (Q2) = 0.7V
The voltage from VCC charges C1 to 5V
VC1 = 4.3V
0.7V
5V

## Slide 16: Oscillator
Positive of C2 is connected to GND (due to Q2 is ON)
VCC slowly charges C2 until 0.7V  Q1 ON
0V
0.7V

## Slide 17: Oscillator
VC1 is currently 4.3V
Positive pin returns to 0V
Negative pin goes to minus 4.3V  Q2 OFF
0V
-4.3V

## Slide 18: Oscillator

## Slide 19: CO2015 Amplifier using Bipolar Junction Transistor

## Slide 20: Bipolar Junction Transistor

## Slide 21: BJT as Amplifier

## Slide 22: Voltages in a BJT
VCC , VBB
VC , VB , VE
VBE , VCE , VCB

## Slide 23: Current and Voltage Analysis
E-B: Forward Bias (like diode)
  VBE ≈ 0.7V
Base Circuit
Collector Circuit

## Slide 24: Load Line Analysis
DC & X Axis: VCE = VCC  IC = 0 (Cut off)
DC & Y Axis: IC = VCC/RC  VCE = 0
DC & Characteristic Line: Q-point

## Slide 25: Voltage Division

## Slide 26: Exercise 1
Determine IB ,IC ,IE ,VBE ,VCE and VCB for the given circuit when βDC = 150

## Slide 27: Solution 1

## Slide 28: Exercise 2
Determine IB ,IC ,IE ,VBE ,VCE and VCB

## Slide 29: Solution 2
Assume that the circuit is working linearly

## Slide 30: Solution 2
IC = (VCC – VCE) / RC
Saturation Mode

## Slide 31: Exercise 3
Determine βDC

## Slide 32: Exercise 4

## Slide 33: Exercise 4
Explain why VC is 15V

## Slide 35: Exercise 4

## Slide 36: Exercise 4

## Slide 37: Exercise 4

## Slide 38: Exercise 5