## Slide 1: CO2015 Operational Amplifier (Op-Amp)

## Slide 2: Contents
Operation
Feedback Circuit
Characteristics
Practical Applications

## Slide 3: Basic Op-Amp
Op-Amp = Operational Amplifier
An Op-Amp consist
  Inverting input
  Noninverting input
  Output
Two power supply pins (V+ and V-)

## Slide 4: Op-Amp Gain
Op-Amps have a very high gain. They can be connected open-loop or close-loop.
  Open-loop refers a configuration where there is no feedback from output back to the input. In the open-loop configuration, the gain can exceed 105.
  Closed-loop configuration reduces the gain. In order to control the gain of an op-amp it must have feedback. This feedback is a negative feedback. A negative feedback reduces the gain and improves many characteristics of the op-amp.

## Slide 5: Op-Amp Models
Practical Model
  Zin is very large
  Zout is small
  The gain in open-loop configuration is very high.
Ideal Model (used for analysis)
  Zin = ∞  Iin+ = Iin- = 0; Vin+ = Vin-
  Zout = 0
  The open-loop gain:

## Slide 6: Operation of Op-Amp
The amplitude of Vout is higer than amplitude of Vin.
Same phase
Inversed phase
Notes: The output is the amplifier of the difference between V+ and V-

## Slide 7: Operation of Op-Amp (cont)
The differential signal of 2 inputs is amplified.
When 2 inputs use common signal, the output is zero.

## Slide 8: Real Op-Amp Models
Acm: Common Amplifier

## Slide 9: Non Feedback Circuits (Open Loop)
For the circuits without feedback (i.e. no connection between output and input), the open-loop gain is very large (>105).
The output voltage will easily reach the saturation and the amplitude will be trimmed.

## Slide 10: Negative Feedback Circuits (Close Loop)
In order to control the gain of an op-amp it must have feedback. This feedback is a negative feedback. A negative feedback reduces the gain and improves many characteristics of the op-amp.

## Slide 11: Negative Feedback

## Slide 12: Exercise 1
Characteristics of an Op-Amp is given in the following table. The power supply is ±15V.
Determine Vo
Parameter | Minimum | Typical | Maximum
Output Voltage | ±12V | ±13.5V | 
Input Voltage | ±11V | ±12.5V | 
Output current of shorted-circuit | ±12mA | ±20mA | 

## Slide 13: Exercise 1 - Solution

## Slide 14: Exercise 2
Characteristics of an Op-Amp is given in the following table. The power supply is ±15V.
Determine Vo when Vin=6V
Parameter | Minimum | Typical | Maximum
Output Voltage | ±12V | ±13.5V | 
Input Voltage | ±11V | ±12.5V | 
Output current of shorted-circuit | ±12mA | ±20mA | 

## Slide 15: Exercise 2 - Solution

## Slide 16: Exercise
Calculate the output gain of the circuit if R1 = 100(Ohm) and Rf = 1(KOhm)

## Slide 17: Answer
11

## Slide 18
Refer to the given figure. A dc input signal of –50 mV is applied. You would measure ________ from the inverting input to ground.
  50mV
  1.05V
  -1.05V
  -50mV

## Slide 19: Exercise
Compute the output voltage in the following circuits using ideal op-amp

## Slide 20: Solution

## Slide 21: Exercise
Characteristics of an Op-Amp is given in the following table. The power supply is ±15V.
Determine VX
Parameter | Minimum | Typical | Maximum
Output Voltage | ±12V | ±13.5V | 
Input Voltage | ±11V | ±12.5V | 
Output current of shorted-circuit | ±12mA | ±20mA | 

## Slide 22: Solution

## Slide 23: Op-Amp Datasheet
IC LM358

## Slide 24: Op-Amp Datasheet (IC LM358)
Maximum power supply: ±22V
Maximum input voltage: ±15V
Maximum differential input voltage: ±30V

## Slide 25: Op-Amp Datasheet
IC 741

## Slide 26: Op-Amp Datasheet (A741)
Điện thế hoạt động 3 đến 30  nếu nguồn đôi là ±15V
Điện thế ngõ vào từ (Vcc-) – 0.3 đến (Vcc+) – 1.5
AVD – Large-signal differential voltage amplification
  200V/mV = 200.000
ri – input resistance: 2M
ro – output resistance: 75

## Slide 27: Output Voltage Threshold

## Slide 28: Practical Op-Amp Circuits
Voltage Follower or Voltage Buffer or Unity Follower
Summing Amplifier
Integrator (Low pass filter)
Differentiator (High pass filter)
Comparator

## Slide 29: Summing Amplifier

## Slide 30: Integrator

## Slide 31: Differentiator

## Slide 32: Comparator
Vout = +Vout(max) when V+ > V-
  Vin > VREF
Vout = -Vout(max) when V+ < V-
  Vin < VREF

## Slide 33: Noisy Comparator
Unexpected pulses

## Slide 34: Noiseless Comparator
Hysteresis
   if Vin is greater than threshold
   if Vin is smaller than threshold

## Slide 35: Noiseless Comparator
Hysteresis
  0 1 if Vin is greater than β threshold
  1  0 if Vin is smaller than α threshold

## Slide 36: Application (1)
Protection Circuit using Op-Amp Comparator

## Slide 37: Application (2)
Analog to Digital Conversion

## Slide 38: IC 555

## Slide 39: IC555 – Clock Pulse Generator

## Slide 40: IC555 – Delay Circuit

## Slide 41
Calculate the input voltage if the final output is 10.08 V
  0.168V

## Slide 42: Bài 3: Đáp án câu A và C
Vo = Av(2-3) = - (âm)
Av rất lớn nên Vo sẽ bị xén ở điện thế ngõ ra nhỏ nhất
Vo = V-(sat) = -13.5V