## Slide 1: CO2015 Basic Electronic Circuit Components

## Slide 3: Actually....
Circuit Analysis
Electronics Components
  Resistor, Capacitor, Transistor
Hardware computer Exercise
  Design and Layout the Circuit
20% for Midterm, 30% for Labs and 50% for final term
Labs are very important (5 hour/ week)
  Don’t share your report!!!!

## Slide 4: Some projects

## Slide 5: Complicated Project
https://ubc.sgp1.cdn.digitaloceanspaces.com/Altium/Altium%20Designer%2020.1.11%20Build%20218.zip

## Slide 6: Basic Electronic Circuit Components
Wires, Cables, and Connectors
Batteries
Switches
Resistors
LED (Light Emitted Diode)
Exercises
Pull up and Pull down resistors

## Slide 7: Solid Core Wires
Strong
High current

## Slide 8: Solid Core Applications

## Slide 9: Stranded Wires (Multicore Wires)
Soft
Smaller current
Easy to Draw

## Slide 10: Braided Wires
Soft and High current

## Slide 11: Coaxial Cables
High speed communication systems

## Slide 12: Twisted Pair Cables
Pulse noise avoidance
ADSL Modem (RJ45)

## Slide 13: Battery
The most popular storage device

## Slide 14: Rechargeable Batteries
Battery capacity: 3500mAh

## Slide 15: Super Capacitors

## Slide 16: Rechargeable Batteries vs Super Capacitor
500 recharge cycles
Difficult to estimate the state of charge
Low leakage current
500 000 recharge cycles
Easy to estimate the state of charge
High leakage current
[CapXX]
[Cymbet ]

## Slide 17: New Generation of Batteries
IC Rechargeable Batteries
Hybrid Batteries (Batteries + Capacitors)

## Slide 18: Switch
A switch is a mechanical device that interrupts or diverts electric current flow within a circuit

## Slide 19: Switch Applications (1)
Here’s a simple home security alarm that’s triggered into action (buzzer and light go on) when one of the normally open switches is closed. Magnetic reed switches work particularly well in such applications.

## Slide 20: Switch Applications (2)
Here’s a switch network that allows an individual to turn a light on or off from either of two locations. This setup is frequently used in household wiring applications.

## Slide 21: Switch Application (3)
A DPDT switch, shown here, can be used to reverse the direction of current flow. When the switch is thrown up, current will flow throw the left light-emitting diode (LED). When the switch is thrown down, current will flow throw the right LED. (LEDs only allow current to flow in one direction.)
SW1
SW2
LED2
LED1

## Slide 22: Resistors
Resistors are electrical devices that act to reduce current flow and at the same time act to lower voltage levels within circuits.
  The relationship between the voltage applied across a resistor and the current through it is given by V =IR.
Resistors may have fixed resistances, or they may be designed to have variable resistances. They also may have resistances that change with light or heat exposure (e.g., photo-resistors, thermistors).

## Slide 23: Resistors

## Slide 24: Understanding Resistor Labels

## Slide 25: Examples

## Slide 26: Examples

## Slide 27: Examples

## Slide 28: Variable Resistors
Special kinds of variable resistors include
  Potentiometers;
  Rheostats; and
  Trimmers.
Potentiometers and rheostats are essentially the same thing, but rheostats are used specifically for high-power ac electricity, whereas potentiometers typically are used with lower-level dc electricity. Both potentiometers and rheostats are designed for frequent adjustment.
Trimmers, on the other hand, are miniature potentiometers that are adjusted infrequently and usually come with pins that can be inserted into printed-circuit boards.

## Slide 29: Photo-Resistors and Thermistors

## Slide 30: Light Emitted Diode (LED)

## Slide 31: Optical Touch LED Matrix

## Slide 32: LED and Resistor Calculation

## Slide 33: LED and Resistor Calculation

## Slide 34: LED Applications

## Slide 35: Exercise 1
Analyze the circuit

## Slide 36: Exercise 2

## Slide 37
An LED which has the characteristics shown in this graph is to be used in the circuit below in which both VS and R can be varied. For this LED the switch on voltage (VD) is 1.7 volt which produces a current of 10 mA at which point the LED will just glow dimly. Let us say that the LED operates brightly at 40 mA, but will fail if the current exceeds 90 mA for too long.
Initially the power supply is set at Vs = 6V. What value is required for the resistor so that the LED operates at 40 mA?
If a current of 20 mA is flowing and the resistor is 200 Ohm, what is the supply voltage?
Find the minimum value of the resistor that could be used without damaging the LED

## Slide 38: Pull Up and Pull Down Resistor
Pull-up and Pull-down resistors are used to correctly bias the inputs of digital gates to prevent them from floating about randomly when there is no input condition

## Slide 39: Pull-up Resistors
Short circuit
Good connection

## Slide 40: Calculating Pull-Up Resistor Value
TTL 74LSxxx series:
  Input high: VIH(min) = 2.0V, IIH = 20µA
  Input low: VIL(max) = 0.8V, IIL= 0.4mA
Single Gate Pull-up Resistor Value
Multiple Gate Pull-up Resistor Value (10 inputs)
Notes: For a high logic, the voltage must be higher than VIH Min and I IH

## Slide 41: Calculating Pull-Up Resistor Value
A Pull-down resistor works in the same way as the previous pull-up resistor, except this time the logic gates input is tied to ground, logic level “0” (LOW)

## Slide 42: Example
TTL 74LS00 NAND Gates along with a single-pole double-throw switch are to be used to make a simple set-reset bistable circuit signal. Calculate: 1). The maximum pull-up resistor values if the voltage representing a logic HIGH input is to be held at 4.5 volts when the switch is open, and 2). The current flowing through the resistor when the switch is closed (assume zero contact resistance). Also draw the circuit.
Data given: Vcc = 5V, VIH = 4.5V, and IIH(max) = 20μA

## Slide 43: Answer
Set-Reset Bistable Circuit

## Slide 44: Programming Arduino

## Slide 45: Programming on BBC Microbit

## Slide 46: Lab Manual
Take randomly 10 resistor pictures
Determine the resistance based on its colors
No | Picture | Value
1 |  | 620Ohm

## Slide 47: Circuit Simulation on TINA TI
TINA-TI setup file: http://cse.hcmut.edu.vn/vtphuong/EDAC/Tina90-TIen.exe
Quick manual
https://www.youtube.com/watch?v=u7_RP1f82oo

## Slide 48: Arduino Programming
Student can simulate at https://www.tinkercad.com/