## Slide 1: CO2015 Field Effect Transistor

## Slide 2: Field-Effect Transistor (FET)

## Slide 3: JFET

## Slide 4: JFET Operations
G and S always in reversed-bias:
  VGS is negative: Depletion area is increased  Resistance between D and S is increased
  VGS is increased (to Zero): Depletion area is decreased  Resistance between D and S is decreased
G and S is in forward-bias:
  JFET likes a resistor

## Slide 5: JFET Operations

## Slide 6: JFET Characteristics
JFET n-channel has three operation modes when VDS >0
A. VGS = 0, JFET is in saturation, ID=Max
B. VGS < 0, JFET is in linear status, ID↓
C. VGS =-Voff, JFET is OFF, ID=0

## Slide 7: JFET Saturation Mode
VGS = 0V, VDD is increased slowly
  Linear region A-B: VDS = RID
  Saturation region B-C: ID is constant
  Pinch off region due to the increase of depletion area.

## Slide 8: Cut-off State
Reversed-bias: 0 < VGS < VGS(off)
  Depletion area is increased  closer to Pinch-off state

## Slide 9: JFET Characteristic

## Slide 10: JFET Transfer Curve

## Slide 11: JFET vs. BJT

## Slide 12: Example
JFET normal state
Determine depletion area in follows:

## Slide 13: Answer
First figure: Forward-bias  depletion area is wider
Second figure: Inverse-bias  depletion area is narrower

## Slide 14: Example
Determine JFET pins
Notes: The left-most terminal on this JFET is the gate, and the other two are source and drain. This is a P-channel JFET

## Slide 15: Example
Determine the correct type (p-channel or n-channel) of the following JFETs and its state (ON or OFF)

## Slide 16: Answer

## Slide 17: Example
Determine the LED status (ON or OFF) regarding each position of switch.

## Slide 18: Answer
ON State: VGS = 0V (Saturation mode)
Next: OFF state: Inversed-bias with very negative VGS

## Slide 19: Example
Determine VDS
Determine VS

## Slide 20: Answer
VDS = VDD – IDRD – ISRS

## Slide 21: Exercise
Determine
Notes: Example 7.2 (page 429 Textbook 11edt)

## Slide 22: Exercise
Determine
Notes: Example 7.2 (page 429 Textbook 11edt)

## Slide 23: Example
Determine VGS and ID

## Slide 24: Answer
Determine the Load line
  ID = 0
  ID = IDSS
  Q is the intersection point of the load line & transfer curve.
    ID = 5.07 mA
    VGS = -2.3V

## Slide 25: Home Work
Determine VGS and VDS for the given JFET, where
  IDSS = 5mA and VGS(off) = -4V

## Slide 26: D-MOSFET

## Slide 27: D-MOSFET Operations (N type)

## Slide 28: D-MOSFET Operations (P type)

## Slide 29: E-MOSFET

## Slide 30: E-MOSFET Operations

## Slide 31: E-MOSFET Transfer Curve

## Slide 32: Example
Determine k, ID, VGS and VDS for given E-MOSFET where
  VGS(on) = 4V and ID(on) = 200mA
  VGS(th) = 2V (=VT)
Hint:

## Slide 33: Answer

## Slide 34: E-MOSFET Datasheet

## Slide 35: JFET Bias

## Slide 36: MOSFET Bias

## Slide 37: MOSFET Operation Status
MOSFET type |  |  | 
N-Channel D-MOSFET | ON | ON | OFF
N-Channel E-MOSFET | ON | OFF | OFF
P-Channel D-MOSFET | OFF | ON | ON
P-Channel E-MOSFET | OFF | OFF | ON
MOSFET type |  |  | 
N-Channel D-MOSFET | ON | ON | OFF
N-Channel E-MOSFET | ON | OFF | OFF
P-Channel D-MOSFET | OFF | ON | ON
P-Channel E-MOSFET | OFF | OFF | ON

## Slide 38: Example
Determine the correct type (p-channel or n-channel, D-type or E-type) of the following MOSFETs

## Slide 39: Answer

## Slide 40: Reference